BỘ GIÁO DỤC VÀ ĐÀO TẠO                                                                           TRƯỜNG ĐẠI HỌC GIAO THÔNG VẬN TẢI

THÔNG TIN LUẬN ÁN TIẾN SỸ                                                              CỦA NCS VŨ MINH ĐỨC

Tên đề tài luận án: “Nghiên cứu, đánh giá độ tin cậy của trạm trộn và xác định một số thông số kỹ thuật hợp lý của buồng trộn thuộc trạm trộn BTNN do Việt Nam chế tạo”

Chuyên ngành: Khai thác, bảo trì thiết bị xây dựng, nâng chuyển

Mã số: 62.52.45.01

Họ và tên NCS: Vũ Minh Đức

Người hướng dẫn khoa học:

1. PGS-TS Nguyễn Đăng Điệm

2. PGS-TS Vũ Thế Lộc

Đơn vị đào tạo: Trường Đại học Giao thông vận tải

NHỮNG KẾT QUẢ MỚI CỦA LUẬN ÁN:

1. Luận án ứng dụng Lý thuyết độ tin cậy đánh giá độ tin cậy của các khối máy chính và tổng thể trạm trộn Bê tông nhựa nóng chế tạo và khai thác ở Việt Nam.

Thống kê được những  hỏng hóc thường gặp, nguyên nhân và giải pháp khắc phục; đánh giá mức độ tin cậy của các khối máy thuộc hệ cơ khí trên các trạm trộn, chỉ ra những khối máy có độ tin cậy thấp hơn, từ đó có hướng để tập trung giải quyết nâng cao độ tin cậy.

2. Đề xuất công thức tính toán công suất dẫn động buồng trộn phản ánh cơ bản các thành phần trở lực, đơn giản và thuận lợi cho vận dụng. Kết quả tính toán theo công thức mới sát với giá trị thực tế.

3. Luận án đã phát triển hướng ứng dụng lý thuyết mô hình đồng dạng và quy hoạch thực nghiệm nghiên cứu ảnh hưởng một số thông số kỹ thuật đến công suất dẫn động buồng trộn BTNN; Xác định các giá trị hợp lý của một số thông số kỹ thuật của buồng trộn Bê-tông nhựa nóng chế tạo tại Việt Nam theo mục tiêu chi phí năng lượng riêng thấp nhất và đảm bảo độ trộn đều của mẻ trộn.

Ministry of Education and Training                                                                  University of Transport and Communications

INFORMATION OF DOCTORAL DISSERTATION                                                                                  BY Ph.D CANDIDATE Vu Minh Duc

Research title:  Research, assess the reliability of the mixing plants and determine some reasonable specifications in the mixing chambers of the hot asphalt mixing plants manufactured in Vietnam

Speciality: Exploitation and maintenance of constructing and raising equipments

Code: 62.52.45.01

Ph.D Candidate: Vu Minh Duc

Supervisors:     1. As.Dr.Prof: Nguyen Dang Diem

2. As.Dr.Prof: Vu The Loc

Education Establishment: University of Transport and Communications

The latest results of the thesis:

1. The thesis applies the theory about reliability to evaluate reliability of main machine blocks and entire hot asphalt concrete mixing plant manufactured and exploited in Vietnam.

The study also lists common faults, causes and solutions, evaluates the reliability of machine blocks belonging to mechanical system in the mixing plant, indicates the machine blocks with lower reliability, from there finds out the ways to improve the reliability.

2. The study also proposes formulas to calculate driving power of mixing booth basically reflecting resisting force components, which are simple and convenient to use. The result calculated by the new formula is close to the actual value

3. The thesis develops theoretical application of similar model and experimental emplacement to study the influence of some technical specifications on driving power of BTNN mixing booth; Reasonable values of some technical specifications of hot asphalt concrete mixing plant manufactured in Vietnam are defined according to the aim at the lowest specific energy cost and ensuring the well-mixing up of each batch.